## Slide 1: Corrosion
Definition: Corrosion is the process of gradual deterioration of a metal from its surface due to the unwanted chemical or electrochemical interaction of metal with its environment.
For example, formation of a layer of reddish scale of hydrated ferric oxide (Fe2O3.H2O) on the surface of iron also known as “rusting of iron” .Another example is the formation of green layer of basic carbonate(CuCO3+Cu(OH)2) on the surface of Cu when exposed to moist air containing CO2.

## Slide 2
Causes of corrosion : Metal exist in nature in the form of oxides ,sulphides and carbonates. These chemically combined states of metal known as ‘ore’ has low energy and is thus thermodynamically stable state for metal. A considerable amount of energy is required during metallurgy. The extracted metal has higher energy and thus it is thermodynamically unstable state .Thus it is natural tendency of metal to go back to the thermodynamically stable state.Metals do this by interacting chemically or electrochemically with their environment to form surface compound and thus undergo corrosion.

## Slide 3
Ore of metal Pure metal Corroded metal
(Stable state) (unstable state) more stable
than pure metal

## Slide 4: Type of corrosion
Corrosion are of two types
1.Direct chemical corrosion or dry corrosion
2. Electrochemical corrosion or wet corrosion
1. Direct chemical corrosion : When metal surface is in immediate proximity to atmosheric gases or anhydrous liquid,a direct chemical interaction between the two leads to chemical or dry corrosion. Dry corrosion are of three types.
Corrosion by O2
Corrosion by other gases
Liquid metal corrosion

## Slide 5
a. Corrosion by O2 : It takes place in absence of moisture.
2M + nO2 2 Mn+ + 2n O-2 M2On
Metal oxide
At low temperature alkali and alkaline earth metals are oxidised and at high temperature,except Ag ,Au and pt,all other metals get oxidised.
A thin layer of oxide formed at the surface of metal can be
i. Stable, like the oxide film on Cu or Al,it acts as a protective coating and thus further corrosion is prevented.
ii. Unstable and decomposes back to metal and oxygen.That is why Ag,Au and Pt do not undergo oxidation corrosion.

## Slide 6
iii. Volatile, the moment it is formed it gets volatilized and metal surface again gets exposed for further attack leading to continous and rapid corrosion.
eg 2Mo + 3O2 2 MoO3
volatile
Hence Mo undergoes excessive corrosion .
iv. Porous, hence further attack through cracks or pores continues and hence the corrosion continues till the entire metal is corroded to metal oxide. Eg Li,
Na, K, Mg etc.

## Slide 7
b. Corrosion by other gases : In addition to O2, other gases like SO2 , CO2 , Cl2, H2S, F2 etc also causes corrosion . The extent of corrosion depends on the chemical on the chemical affinity between the metal and the gas involved. The degree of attack depends on the formation of protective or non-protective films on the metal surface.
If the film formed is protective or nonporous, eg
Agcl film (resulting from the attack of cl2 on Ag
metal)
b. If the film formed is non-protective or porous , the
surface of the whole metal is gradually destroyed.
For example, dry cl2 gas attack on tin (Sn) forming

## Slide 8
Sncl4 which volatilizes immediately, thereby leaving fresh metal surface for further attack. Similarly, in Petroleum industry, H2S at high temperature attacks steel forming FeS scale which is porous.
c. Liquid metal corrosion : This type of corrosion occurs due to chemical action of flowing liquid metal at high temperature on solid metal or alloy. Such corrosion occurs in devices used for nuclear power. It causes weakening of solid metal .

## Slide 9
2.Wet or Electrochemical corrosion: This Type of corrosion occurs ( i). where a conducting liquid is in contact with metal or (ii).when two dissimilar metals or alloys are either immersed or dipped partially in a solution. This corrosion occurs due to the existance of separate ‘anodic’ and ‘cathodic’ areas between which current flows through the conducting solution. At anode free electrons are liberated and oxidation takes place . So anodic metal is destroyed by either dissolving the metal in the form of +ve ions in the solution or reverting the metal to a combined state such as oxide. Hence corrosion occurs at anode.

## Slide 10
At cathode gain of electrons occurs and reduction takes place. Cathode reactions do not affect the cathode. At cathodic part,dissolved constituents in the conducting medium accepts the electrons to form ions like OH- . The metallic ions (at anodic part) and non-metallic ions (at cathodic part) diffuse towards each other through conducting medium and form a corrosion product.

## Slide 11
O2 + Fe2+ 2OH- ½O2 +2e +H2O
Fe2O3 Fe+2 Fe+2 cathode
anode Fe Fe
4e-
2e- 2e-

## Slide 12: Corrosion control
Following methods are used for protection against corrosion
1. Proper designing : Important design principles are:
i. Contact of dissimilar metals in presence of a corroding
solution should be avoided.
ii. If two dissimilar metals have to be used, they should be
as close as possible to each other.
iii. Whenever the direct joining of dissimilar metals is
unavoidable, an insulating fitting may be applied in
between them to avoid direct metal metal electrical
contact.

## Slide 13
iv. The anodic metal should not be painted or coated, when in contact with a dissimilar cathodic metal, because any break in coating would lead to rapid localized corrosion.
v. It is desirable that the design allows for adequate cleaning and flushing of the critical parts.
vi. Whenever possible, the equipment should be supported on legs to allow free circulation of air and prevent the formation of damp areas.

## Slide 14
2. Using pure metal : Impurities in a metal causes heterogeneity ,which decreases corrosion –resistance of the metal. Thus, the corrosion- resistance of a given metal may be improved by increasing its purity. Generally, purification of metals is of use only under conditions in which corrosion by a purely electrochemical mechanism and not by direct chemical attack.
3. Using metal alloys : Precious metals such as platinum and Gold are corrosion resistant. Corrosion resistance of most metals is best increased by alloying them with suitable elements, but for maximum corrosion resistance ,alloy should be completely homogeneous.Cr is the best suitable alloying metal for Fe and steel.

## Slide 15
4. Cathodic protection : The principle involved in this method is to force the metal to be protected to behave like a cathode,thereby corrosion does not occur. Thereare two types of cathodic protections.
i. Sacrificial anodic protection method : It this method, the metallic structure is connected by a wire to a more anodic metal , so that all the corrosion is concentrated at this more active metal. The active metal itself gets corroded slowly, while the parent structure is protected. The more active metal so emplyed is called “Sacrificial anode”. Metals commonly employed as sacrificial anodes are Mg,Zn,Al and their alloys .

## Slide 16
Important applications of sacrificial anodic method include protection of buried pipelines, underground cables, marine structure, water-tanks etc.
ii. Impressed current cathodic protection : In this method , an impressed current is applied in opposite direction to nullify the corrosion current,and convert the corroding metal from anode to cathod. Usually, the impressed current is derived from a direct current source (like battery) with an insoluble anode(like graphite, stainless steel or platinum).Sufficient d.c.current is applied to an insoluble anode, burried in the soil and connected to the metallic structure to be proected.

## Slide 17
This type of cathodic protection has been applied to water-tank,buried oil or water pipes, condensers etc. This type of protection technique is particularly useful for large structures for long term operations.
5. Application of Protective coatings: Two important protective coatings are given below :
i. Anodic coatings : It is produced from coating metals, which are anodic to the base metal.eg coating of Zn, Al and Cd on steel are anodic , because their electrode potentials are lower than that of the base metal.eg in case of galvanised steel, Zn is attacked, leaving underlying iron unattacked.

## Slide 18
Corrosive environment
exposed part(cathode)
Zn coating Zn Zn+2 + 2e-
e- e-
unexposed part(anode)

## Slide 19
ii. Cathodic coating : cathodic coating are obtained by coating a more noble metal (ie having higher electrode potential) than the base metal. Cathodic protection provides effective protection to the base metal only when they are completely continuous and free from pores,breaks or discontinuities.
If such coatings are punctured, much more corrosion damages can be done to the base metal than to the metal without it.eg a tin-coatin on a sheet of iron provides protection only as long as the surface of the metal is completely covered. However if the surface coating is punctured, the tin becomes

## Slide 20
the cathode,while exposed iron (which is above tin in electromotive series ) acts as anode. A galvanic cell is set up and an intense corrosion at the exposed part occurs.
Corrosive environment
exposed part (anode)
Fe Fe+2 + 2e-
Sn coating
e- e-
Unexposed part (cathode)