## Slide 1: DYES
Definition : Dyes are those coloured compounds that can be firmly fixed to the fabrics by chemical or physical bonding.
Classification : Dyes can be classified according to the method of Application as
1.Direct Dyes 2. Mordant Dyes 3. Vat dyes 4.Ingrain Dyes 5. Disperse Dyes

## Slide 2
1.Direct Dyes : Direct Dyes can be directly applied to the fabrics from their aqueous solution. These are suitable for those fabrics whose constituents can form hydrogen bonds with the dye, e.g. Nylon, Rayon, Silk, Wool and cotton. E.g. Naphthol Yellow and Martius Yellow.
2. Mordant Dyes : Mordant Dyes impart different colours to the fabric in the presence of different metal ions (called as mordants). These dyes produce wash fast colours, when applied after treating the fabric with mordant.
For example Alizarin is a mordant dye. It gives blue colour to the fabric already treated with barium salt solution. But it imparts rose red colour to the fabric which is treated with aluminium salt solution.

## Slide 3
Dying with Mordant dye : Fabric is first impregnated in mordant solution (say Al(OH) 3 solution in presence of wetting agent). When the cloth mordanted with aluminium salt is dipped in a tub containing dye , the mordant co-ordinates to the basic (or acidic) group in the fabric and then combines with acidic (or basic) dye. This is responsible for imparting washfast colour to the fabric. In fact, chelation is responsible for the alteration in the anergy levels of dye, that is why same dye can give different colours in the presence of different mordants.

## Slide 5
3. Vat dye : Vat dyes are water insoluble coloured compounds which upon reduction give soluble product. The reduction products have affinity for specific fabrics. On exposure to the air, the coloured insoluble dye is reformed which remain firmly fixed on the fabric.

## Slide 6
Dying with Vat dyes : In applying a Vat dye to the fabric, the dye is reduced with suitable agent like sodium hydrosulphite. The reducing operation was formerly carried out in wooden vat’s, giving rise to the name ‘Vat dye’. The fabric is dipped into the reduced dye . The dye attaches itself to the fabric. Reoxidation is then done by its exposure to air or any other oxidizing agent. Coloured insoluble dye is reformed which remains firmly fixed in the fibre .
Indigo is oldest dye known and is a vat dye.

## Slide 8
4. Ingrain dyes :These dyes are synthesized within the fabric and may be applied to any type of fibre. The azo dyes (containg –N=N- group) are good examples of ingrain dyes. The cloth to be dyed is first soaked in an alkaline solution of a phenol and dried. It is then immersed in a cold alkaline solution of a diazonium salt. Coupling reaction takes place within the fabric. Since these dyes are insoluble in water, they are very fast. E.g. Aniline Yellow and Butter Yellow.

## Slide 10
5. Disperse Dyes : These dyes are applied in the form of a dispersion of finely divided dye in a soap solution in the presence of some stabilizing agent such as phenol,cresol or benzoic acid. The absorption into the fibre is carried out at high temperature and pressure. Disperse dyes are used to dye nylon, polysters, Dacron and other synthetic fibre.Anthraquinone dyes eg celliton Fast Pink B and celliton Fast Blue B are example of disperse dye.

## Slide 13
Raw Materials for the manufacture of dyes : The raw materials for the manufacture of dyes are mainly Benzene , Toluene ,Naphthelene, Anthracene and Phenol. In the past , these compounds came exclusively from the distillation of coal-tar , but in recent years increasing quantities especially of benzene and toluene have become available from petroleum and natural gas. A variety of inorganic materials are also required by the dye industry. These include sulphonic acid, oleum, sodium nitrite, nitric acid, chlorine, bromine, caustic soda, hydrochloric acid, sodium bicarbonate and manganese dioxide.

## Slide 14
Non –Textile uses of Dyes : Dyes are used in many ways other than for dying fabrics. Large quantities of dyes are consumed by paper industry. Natural leather can also be dyed with direct dyes.
Dyes for many materials such as gasoline, lacquers and varnishes are selected on the basis of solubility and fastness.

## Slide 15
Important and growing markets for dyes are the plastic and metal industries . Dyes are used as indicators for the control of chemical processes. They are also used for staining biological substances,printing inks and colour photography.
Dyes for food, drugs and cosmetics must be chosen with great care to avoid toxic effects. In India dyes are certified by the government when judged safe for such uses. Only the certified dyes may legally be used. This restriction does not apply to natural dyes.