## Slide 1: Electrolysis
Electrolytes: Substances which can conduct electricity in the fused state or in solution and at the same time decomposes during the passage of electric current are called electrolytes.
Electrodes : The metal foil or plates or graphite plates through which current is passed through an electrolyte by immersing it is called electrode.
Anode : Which is connected with the +ve pole of battery.
Cathode : Which is connected with the –ve pole of the battery.
Ion : An ion is an atom or a group of atoms carrying +ve or –ve charge of electricity.

## Slide 2
Electrolysis : Electrolysis is the term employed for chemical decomposition caused by passing an electric current through an electrolyte.
when an electrolyte is dissolved in water or taken in an molten stage it will produce +ve and -ve ion in equal number. Now if an electric current is passed through two electrodes into the solution, the positively charged ions will be attracted to the –ve electrode and the –vely charged ion will be attracted to the +ve electrode.This movement of ions is called electrolytic conduction.
-ve ions are discharged at the anode by loosing electrons. These electrons then move from anode to cathode by the outer source.

## Slide 3
+vely charged ion then discharged at the cathode by accepting electrons. Thus during electrolytic conduction we have electrons flowing through the extra wire and ions flowing through the solution. The flow of electrons are opposite to the direction of current.
Cathode Anode
A+ B-

## Slide 4
Molten NaCl on electrolysis liberates Cl2 at the anode and Na at cathode.
NaCl Na+ + Cl-
At cathode ,
Na+ +e- Na
At anode,
Cl- Cl + e-
2Cl Cl2

## Slide 5: Faradays laws of electrolysis
Michael Faraday during 1832- 33 studied the phenomenon of electrolysis and discovered two fundamental laws which are known as Faraday’s laws.
First law: The mass of an ion liberated during electrolysis is directly proportional to the quantity of electricity which has passed through the electrolytic cell.
If w is the mass in gm of ion
Q is the quantity of electricity in coulomb
C is the strength of current in ampere
t is the time in Second

## Slide 6
Then
W  Q
But Q = C x t
W = C x t
W = Z x C x t
where Z is a constant and called as electrochemical equivalent or ECE.
if C =1 and t = 1 ie 1 ampere of current is passed for 1 seconds then
W = Z
Thus ECE may be defined as the mass in gm of an element liberated by passing 1 ampere of current for 1 second.
Again when 1 ampere of current is passed for 1 second , the quantity of electricity is called 1 coulomb

## Slide 7
Again when 1 ampere of current is passed for 1 second , the quantity of electricity is called 1 coulomb
Coulomb = Ampere x Second
So ECE of an element is the amount of element liberated by 1 coulomb of electricity.

## Slide 8
Problem : A current of 0.5 ampere is passed through a solution of AgNO3 for 30 minutes to precipitate 1.006 gm of Ag .Calculate the ECE of Ag.
W = Zx C x t
Z = -------------
W = 1.006 gm
C = 0.5 ampere
t = 30 x 60 Seconds
 Z = ------------------- = 0.001118 gc-1
W
C x t
1.006
0.5 x 30 x 60

## Slide 9: Second law
When the same quantity of electricity is passed through different electrlytes, the relative masses of ions liberated are proportional to their chemical equivalents.
This law states that if same quantity of electricity is passed through a number of cells , connected in series and containing say CuSO4 ,AgNO3 , Zn(NO3)2 solution respectively , then the relative amounts of the elements liberated will be proportional to their equivalent weights. ie,amount of Cu,Ag & Zn will be 63.6/2= 31.8gm Cu, 108 gm Ag, 65/2=32.5 gm Zn.
Now , Let m1, m2 be the amount of elements A and B liberated during electrolysis and E1 and E2 be their chemical equivalent respectively , then according to second law of Faraday.

## Slide 10
--------------- = ----------------
m1
E1
m2
E2
----------- = ----------
m1
m2
E1
E2 -------1.
or
But from first law m1 = Z1ct and m2 = Z2ct
 --------- = ---------
From equation 1.
------------ = ---------
Thus ----------------------------- = ----------------
m1
m2
Z1
Z2
Z1
Z2
E1
E2
ECE of an element A
ECE of an element B
CE of A
CE of B

## Slide 11
Z  E
Thus ECE of an element is directly proportional to its chemical equivalent.

## Slide 12
From first law we have got that on passing 1 coulomb of electricity ECE of substance is liberated. ie if 1 coulomb of electricity is passed through different solutions like AgNO3 ,CuSO4 and dilute H2SO4acid , the amount of Ag, Cu and H liberated will be
Ag = 0.001118 gm
Cu = 0. 00032935 gm
H = 0. 0000104 gm
Therefore amount of electricity require to liberate gm eq.wt. of these substances will be as follows

## Slide 13
0.001118 gm Ag is liberated by 1 coulomb
108 gm of Ag is liberated by = -------------------
= 96500 coulomb
Similarly,0.00032935 gm of Cu is liberated by 1coulomb
 31.5 gm ,, ,, ,, = ----------------
= 96500coulomb
108
0.001118
31.5
0.00032935

## Slide 14
The amount of electricity require to liberate 1 gm equivalent weight of the element is 96500 coulomb. This 96500 coulomb of electricity is called 1 faraday.
1 Faraday = 96500 coulomb .
Again, 96500 coulomb can liberate = 1 gm eq. wt
 1 ,, ,, ,, ,, = -----------------
= ECE
ECE = -----------------
gm eq. wt
96500
gm.eq.wt.
96500

## Slide 15
Problem :
Atomic weight of Cu is 63.6. What is its ECE ?
Solution:
eq. wt.of Cu = ------------= 31.8
ECE of Cu = -----------------= 0.000329 gm c-1
63.6
2
31.8
96500

## Slide 16
2. Calculate the amount of Cu deposited by 0.5 ampere of current for 30 minutes.(At.wt. of Cu 63.6)
Solution :
C = 0.5 ampere eq. wt. = ---------- = 31.8
t = (30x60) Sec
Z = -------------- = 0.000329
W = .000329x0.5x30x60
= 0.2961gm
63.6
2
31.8
96500

## Slide 17
3. If 3 amperes current deposite 4 gms of Ag in 20 mins. What is the ECE of Ag.
given, C = 3 ampere
W = 4gm
t = 20x60 sec
W = ZCt
or Z = ---------- = -------------------= 0.00111gmc-1
W
Ct
4
3 x 20 x 60

## Slide 18
4. What is the amount of Ag deposited by 5 amp current for 20 mins.( At. wt. of Ag is 108).

## Slide 19: Application of electrolysis in industry
1. Electro-Plating : It is the art of electrolytic depositions of one metal over another for improving the appearance of the metal or for protecting it from corrosion. Thus Iron is generally covered by Ni,Sn or Zn plating to prevent corrosion.
Various household articles are plated with Ag, Cr or
Nickel to enhance their beauty and to protect them from
corrosion.
Process : In order to deposite one metal on another, the metal which is to be plated is thoroughly cleaned and suspended from metal bars in a tank to form cathode. The anode is made of the pure plating metal which is also suspended from the metal bars.The solution in the tank is the salt solution of the plating metal.

## Slide 20
In silver plating the solution of AgNO3 may be used while in Cu plating the solution of CuSO4 may be used.
When electric current is passed the +ve ions of the plating metal migrate to the cathode and are thus deposited around the metal to be plated. The thickness of the deposite depends upon the current density and the duration of the plating.

## Slide 21
2. Electro- metallurgy : Most of the metals are obtained commercially by the electrolysis of metallic ore either in solution or in fused state. This process is known as electro-metallurgy. Na, K, Al, Ca, Mg etc are obtained by this process.
3. Electro-refining of metals : The process of electrolysis is also used for refining of impure metals.This is Known as electro-refining of metal . Several metals such as Cu,Ag,Pb,Al are required with the help of this process.

## Slide 22
4. Galvanisation : The process of coating iron or steel products with a thin coat of Zinc to prevent them from rusting and corrosion is called Galvanisation. Materials which are generally galvanised are sheets, pipes, wires, strips and number of other articles having irreular shape.
5.Manufacture of chemicals and medicine :
Various important chemicals and medicines are prepared by the process of electrolysis. NaOH , Na2CO3 , KClO3 , Ca(OCl)Cl are manufactured electrolytically. Various pigments, medicines such as iodoform etc are manufactured by this process.