## Slide 1: ENVIRONMENTAL CHEMISTRY
Definition of Pollution: Pollution may be defined as undesirable changes in the physical, chemical and biological characteristics of air, water or land that may or will affect the lives of human and other living systems.
There are three main types of environmental pollution. These are
1. Air Pollution 2. Water Pollution 3. Land Pollution

## Slide 2
Pollutants: Anything that causes pollution is a pollutant. Pollutants need not be material substances. Sound, too, can be a pollutant. So, it can be defined as, “Pollutant is a substance, chemical or factor, which has the potentiality to adversely affect natural characteristics of environment, Natural resources and assets.” Pollutant can be of following two types:
1. Degradable Pollutant: Some pollutants are degraded quickly by biological processes. These are called degradable pollutants. Egg. Wood, pulp etc.
2. Non-Degradable Pollutant: Some chemical substances are not degraded by biological processes or are degraded very slowly. These are called non degradable pollutants. Example of such pollutants are DDT, polythene etc.

## Slide 3: WATER POLLUTON
When water contains harmful elements, germs or particles, it is said to be polluted. There has been an alarming increase in the pollution of natural water bodies near large cities and industrial areas. Water pollution is mainly caused by-
1. Natural process in which the decomposed vegetable, animal and weathered products are brought into main water resources and lead to deterioration of natural environment.
2. Anthropogenic processes such as industrial, agricultural, urban, domestic, radioactive mining sources, use of pesticides and fertilizers by man etc. These pollutants are constantly poured in water deteriorating it to such an extent that it becomes unfit for living communities.

## Slide 4: Sources Of Water Pollution
Water, the most abundant and wonderful natural resources, is extremely essential for survival of all living organisms. But today clean water has become a precious commodity and its quality is threatened by numerous sources of pollution, which are as follows-
1. Sewage and Domestic wastes
2. Industrial effluents
3. Agricultural discharges
4. Fertilizers
5. Detergents
6. Toxic metals
7. Siltation
8. Radioactive materials

## Slide 5
1.Sewage and Domestic wastes
Sewage is commonly a cloudy dilute solution containing mineral and organic matter. About 75% of water pollution is caused by sewage, domestic wastes and food processing plants. It also includes human excreta, soap, detergent, metals, glass, rubbish garden waste etc.
2.Industrial effluents
Industrial effluents discharged into water bodies contain toxic chemicals, hazardous compounds, phenols, aldehydes, ketones, amines, cyanides, metallic wastes, plasticizers, toxic acids, corrosive alkalis, oils, greases, dyes, radioactive wastes and thermal pollutants from numerous industries.

## Slide 6
Harmful effects of Industrial effluents
1. Industrial effluents causes deleterious effects on living organisms and may bring about death or sub lethal pathology of kidneys, liver, lungs, brain and reproductive system.
2. Effluents like methyl mercaptan and pentachlorophenol lower the photosynthetic rte of aquatic communities by hindering sunlight penetration into water column,
3. It has been reported that free chlorine discharged by factories near Mirzapur in UP had caused heavy fish mortality in river Sone near Dehrionson in Bihar.
4.

## Slide 7
4. Mercury poisoning among aquatic organism has resulted in crippling and often fatal diseases like Minamata in Japan (1950).
5. Industrial effluents consisting of As, Pb and CN etc cause cellular degeneration in brain , which results in frigidity , coma, stupor and numbness.
6. Effluents containing acid and alkalis make the water corrosive.
7. Toxic effluents may inhibit the natural purification scheme of water bodies.

## Slide 8
5. Siltation : Siltation is the most wide spread and damaging pollutant especially in hill streams. These soil particles create high turbidity’s in water and may hinder the free movement of aquatic organisms , growth of fishes and their productivity.
6. Thermal pollutant : These pollutants include the waste chiefly from atomic, nuclear and thermal power plants. The discharge of unutilised heat is highest in the thermal power plants which adversely affect the aquatic environment.
7. Radioactive materials in water : Today man made sources have begun to add large doses of radioactive materials in water bodies to which the living organism are accustomed with various ill effects.

## Slide 9
Radioactive pollutants enter into water streams from various sources such as nuclear power plants, nuclear reactors, nuclear test, nuclear installations, processing fission and fusion products etc.
The ultimate sink of all polluted water is the ocean. Underground water is considered to be safe, has also not escaped pollution. Industrial waste materials which are dumped on the ground seep through the ground and pollute underground water.

## Slide 10
Biochemical Oxygen Demand
Water pollution is measured by BOD. The polluted water may contain large amounts of inorganic and organic compounds. Some of these can be oxidised by dissolved oxygen in the presence of microorganisms. BOD is a measure of the dissolved oxygen that would be needed by the microorganisms to oxidise the compounds present in water over a period of 5 days at 20oC. A large number of organic and inorganic compounds are resistant to microbial oxidation. They, therefore, don’t contribute to the BOD, though their presence causes water unfit for consumption

## Slide 11
BOD is taken as a realistic measure of water quality. Clean water would have BOD value less than 5ppm whereas highly polluted river water could have BOD value of 17 ppm or more. Drinking water should have BOD less than 1ppm.
In order to find out BOD, the water sample is first saturated with oxygen. It is then incubated at 20oC for five days. This allows time for micro organisms in the water sample to oxidise pollutants. The remaining amount of dissolved oxygen is determined and BOD is obtained by subtraction.

## Slide 12
Chemical Oxygen Demand (COD)
Although BOD test indicates the amount of total organic matter, there are so many drawbacks. To compensate them chemical oxygen demand is carried out. COD is readily measurable parameter for streams and industrial waste studies and control of water treatment plants. The method of measurement of COD depends upon the chemical oxidation of the sample with a strong chemical oxidising agent, such as potassium dichromate (K2Cr2O7) which is capable of oxidising all the organics. COD may therefore, be defined as the amount of oxygen required by organic matter in a sample of water for its oxidation by a strong chemical oxidising agent such as K2Cr2O7.It is expressed in terms of amount of oxygen, in ppm taken from a K2Cr2O7 solution in two hours.

## Slide 13
A known amount of K2Cr2O7 is added to a measured amount of the sample and the mixture is boiled with concentrated H2SO4 . After boiling , the amount of unreacted dichromate is determined by titration against a standard ferrous ammonium sulphate (Mohr’s salt ) solution using ferroin as the indicator . the difference between the dichromate originally present and the dichromate remaining unreacted gives the amount of dichromate used for the oxidation of organic matter.
Textile wastes, paper mill wastes and other wastes having higher levels of cellulose have been found to be have considerably higher COD values than their BOD values , because of the fact that cellulose is not readily attacked in BOD test. COD is important in management and design of treatment plant because of its rapidity in determination.

## Slide 14
Measurement of water quality
Turbidity: Turbidity in water mainly arises from colloidal matter, fine suspended particles and soil erosion. Generally greater the turbidity, stronger is the sewage and industrial effluent concentrations and worst are the effects. Hence the degree of turbidity of a water course may be taken as a measure of the intensity of pollution. However non-turbidity does not mean that water is unpolluted , because clear water may also be heavily contaminated with acids, alkalies etc, which do not cause turbidity.
Turbid water becomes unsuitable for industrial purposes and also for domestic use because Fe, Mn , Ni , Co, Pb, Sb, Bi etc present in it may cause stain on clothes, sinks and baths etc various coagulants like ferric chloride, ferric sulphate, ferric alum etc can check turbidity of water.

## Slide 15
The standard unit of turbidity is considered as that produced by one ppm of silica in by centrifugation.
Ammonia: NH3 is colorimetrically measured using Nessler’s reagent.
Nitrate and nitrite: it is the most essential to monitor nitrate and nitrite regularly in water supplies because they may be potentially hazardous to health if their maximum admissible concentrations (MAC) of 50 mg/L and 0.1 mg/L respectively are exceeded. The presence of NO3 – in water bodies causes disease, known as methemoglobinemia. The permissible limit of NO3- in drinking water is 10 mg/L.
Total nitrate and nitrite is determined by first reducing the nitrates and nitrites to NH3 by Devarda’s alloy (50% Cu, 45% Al, 5% Zn) in strongly alkaline solutions. The NH3 is distilled into excess of standard acid and then estimated spectrophotometrically.

## Slide 16
Testing for sewage (NH3,NO2- , NO3-)
Nitrogen present in waste water is generally in the form of NH3 gas, nitrates and nitrites.NH3 is highly undesirable in streams and lakes. Because it extremely enhances “eutrophication” means excessive algal growth which leads to depletion of oxygen. This results in death of fish and other aquatic life.
The waste water containing NH3 is directed into a metal tower. As this water trickles downwards over a series of small plastic baffle plates, air is forced upwards through the effluent which thereby results in the removal of NH3 gas.

## Slide 17: Air Pollution
According to the latest view point air pollution is defined as “Substances introduced into air by the activity of mankind in such concentrations sufficient to cause serious effects on his health, vegetables, property or interference with the enjoyment of his property.
Air pollution may be caused by nature or by human activities. Natural air pollution can be caused by volcanic eruptions, forest fires and inorganic and organic decays which result in the accumulation of harmful dusts and sulphurous gases in the atmosphere. However this type of pollution existed even before the growth of technology, so it is of little concern to us.
It is the air pollution caused by human activities that has become a cause for concern. This type of pollution is generally localized over industrial centres and over- polluted cities. But its effect is severe. Man-made air pollutants often do not rise above 600 metres, which prevents the dilution of these substances. Consequently, the concentration of harmful substances in the air over cities and industrial centres rises to alarming proportions.

## Slide 18
Air pollutants : There are two types of air pollutants – Gaseous and particulate. Pollutants which are in the gaseous state at normal temperature and pressure are called gaseous pollutants. These are : Oxides of Nitrogen, Oxides of Sulphur, Oxides of carbon, Hydrocarbons etc.
Small solid particles and liquid droplets are collectively known as particulates. These are present in atmosphere in fairly large numbers and pose a serious air pollution problem . Particulate pollutants are fumes ,dust, ash, carbon smoke, lead, asbestos, mist, spray, oil, grease etc .
.

## Slide 19
Besides the above pollutants, there are certain products formed by the atmospheric reactions of hydrocarbons and oxides of nitrogen in the presence of sunlight , which are harmful. These are called secondary pollutants , eg Ozone.
Sources of air pollution :
Sources of air pollution can be devided into three classes (a) Stationary combustion sources (b) Mobile combustion sources and (c) Industrial processing and other sources.
Stationary combustion sources : The burning of fuel like coal and petroleum products produces gaseous and particulate air pollutants.
.

## Slide 20
Coal is mainly carbon with some incombustible minerals like Sulphur and nitrogen. When it is burnt , carbon dioxide , carbon monoxide and water is produced . Mineral ashes are also produced and some of these mix with air to form fly ash. Sulphur present in fuel produces mainly SO2 and SO3 . These gases react with water to form Sulphurous acid sulphuric acid and when they mix with rain they form what is known as acid rain .
Nitrogen dioxide and nitric oxide are produced when nitrogen present in fuel gets oxidised. Dissolution of nitrogen dioxide in rain too, leads to acid rain.
The incomplete combustion of petroleum often produces many other gaseous and particulate pollutants. The particulate pollutants are mainly carcinogenic.

## Slide 21
Mobile combustion Sources : Automobile, locomotives and aircraft are the major mobile combustion sources . In cities , the rapid growth of vehicular traffic has made the problem of air pollution very intense . The combustion of fuel in the engines of vehicles produces various pollutants , the major ones being CO , oxides of nitrogen and hydrocarbons. The gasoline used in cars contains antiknock compounds like tetraethyl lead Pb(C2H5)4 , which produce toxic particulate lead cpmpounds.
The incomplete combustion of gasoline and diesel in vehicular engines produces many substances , which undergo photochemical reactions with oxides of nitrogen to produce photochemical smog . This smog is very toxic.

## Slide 22
Industrial processing and other sources : Chemical industries produce numereous air pollution. The major pollutants are CO, oxides of sulphur various particulates. Industries where organic chemicals are processed at high temperature release many other gases. Compounds containing chlorine and fluorine , like chlorofluoro methane used as refrigerants and in air – sprays are causing the depletion of ozone layer in stratosphere.

## Slide 23: Green house effect
Green house effect is the phenomenon in which earth’s atmosphere traps the heat from the sun and prevents it from escaping into the outer space. The green house effect received its name because the earth’s atmosphere acts much like the roof of a green house.Sunlight enters a green house through the transparent roof and heats the plants but the heat emitted by the plants in the form of infrared radiation can not pass through the roof. As a result inside temperature increases. Similarly the earth’s atmosphere allows most of the sunlight that falls on it to pass through and heat the surface. An increase in average global temperature is likely to increase the incidence of infections diseases such as malaria, sleeping sickness,dengue and yellow fever etc.

## Slide 24
Ozone layer depletion:
Ozone (O3), a light bluish gas found in the stratosphere, absorbs ultraviolet radiation of the sun which is harmful to the living things . O3 therefore, acts as one of the earth’s most important live support systems. In recent years , however, there have been reports of the depletion of this protective ozone layer. The effects of the depletion of ozone layer in the stratoshere include increased human cataracts, skin cancer, reduction of planktons in ocean water, depletion of plants and crops.
The major cause of ozone layer destruction is believed to be the release of chlorofluorocarbon compounds (CFC) , also known as freons, into the atmosphere .

## Slide 25
The decomposition products of CFC’s destroy ozone as below.
CF 2 Cl2(g) + hυ Cl. (g) + .CF2Cl (g)
Cl. (g) + O3(g) ClO.(g) + O2(g)
ClO.(g) + O(g) Cl.(g) + O2(g)
These chlorine atoms are free to react with more ozone. It has been shown that over one thousand ozone molecule can be destroyed by one Cl. Great loss of ozone has occurred since the early 1980s in the ozone layer over Antarctica producing massive ozone hole which occurs during springtime replenishes after spring .

## Slide 26
Soil Pollution :
Soil pollution directly affects the growth of plants. It also affects health . The cause of soil pollution are
1.The dumping and disposal of wastes and garbage are major sources of soil pollution. The innumerable pathogens present in wastes contaminate soil and crops and consequently harm human beings and domestic animals .
2.Excessive use of pesticides and fertilizer also pollutes land. Pesticides reduce the population and the number of species of living organisms and thus affect the fertility of the soil. Several pesticides and their degradation products are absorbed by plants, which affects the entire food chain .

## Slide 27
. The harmful pesticides and their degradation products accumulate in the fatty tissues of human and affect the nervous system . Residue of excess fertilizers also herm the growth of plants .
3. Many industries also cause soil pollution . “Fly ash” from industries which settles over soil and plants has a toxic effect .The exploration of crude oil produces wastes which make the entire area unfit for cultivation .
4. Another source of soil pollution is the open cast mining of coal . Mining leads to loss of grazing and fertile land , soil erosion from waste dumps ,sedimentation , damage to flora and fauna as well as water and soil pollution.

## Slide 28
Soil Pollutants :
1.Industrial pollutants : These are mainly discharged from pulp and paper mills ,
chemical industries oil refineries , sugar factories , textiles and steel industries , coal, cement and petroleum industries etc . Thermal , atomic and electric power plant also add pollutants to soil . The furnaces of such industries generate ‘fly ash’ ie unburnt brownish black substance which severely pollute air ,water and soil. Industrial wastes mainly consist of organic compounds along with inorganic complexes and non – biodegradable materials . These pollutants affect and alter the chemical and biological properties of soil which finally lead to serious affects on living organisms.

## Slide 29
2. Radioactive pollutants : Radioactive substances resulting from explosions of nuclear devices, atmospheric fallout from nuclear dust and radioactive wastes penetrate the soil and accumulate there creating soil pollution . Radio -nuclides of radium, thorium, uranium , isotopes of potassium (K-40) and (C-14) are very common in soil. Radioactive waste contain several radio nuclides such as strontium -90, iodine -129 , caesium – 137 etc which are most injurious .
3. Agricultural pollutants : Today with the advancing agro –technology ,huge quantities of fertilizers pesticides , herbicides , weedicides and soil conditioning agents are employed to increase crop yield .These chemical agents contain severe toxic metals like lead, arsenic , cadmium , mercury and cobalt etc .

## Slide 30
When these chemical s are applied to a land the metal will accumulate on the soil permanently ,there by introducing these into growing crops.
4. Biological pollutants : Soil gets large quantities of human , animals and birds excreta which constitute the major source of land pollution by biological agents . These biological agents are highly responsible for heavy contamination of soil and crops by pathogens. In developing western countries , intestinal parasites constitute the most serious soil pollution problem .

## Slide 31: Prevention and control of pollution
Control of air pollution : Air pollution may be controlled in two ways : i) By separating the pollutants before releasing the gas mixture into the air and ii) By converting pollutants into harmless products at the source .
Particulate pollutants can be separated by using gravity settling tanks , porous filters, cyclone collectors or electrostatic precipitators . But separating gaseous pollutants from harmless gases is not easy . Only some pollutants , like ammonia gas , can be separated by dissolving them in water .

## Slide 32
Various chemical methods can be used to convert pollutants into harmless products at the source . The most important of these is the oxidation of pollutants in air . Another chemical method is the neutralization of acidic or basic compounds before their release into the atmosphere . Air pollution can not be controlled totally as it is mostly the result of industrial activities which are associated with progress and prosperity. However, it can definitely be checked by establishing standard guidlines and regularly monitoring the pollution level . The environmental laws which has been established should be strictly enforced .

## Slide 33
Control of water pollution : The most important step that has to be taken to control water pollution is the treatment of sewage before its ultimate disposal in nature . during treatment, suspended particles have to be removed, organic compounds have to be decomposed and bacteria and other toxic materials have to eliminated. Sewage treatment is quite expensive and poses a problem for developing countries like India .
The other step is to enforce the law that industrial waste must be processed before being disposed of.

## Slide 34
Control of soil pollution :
1. Soil pollution can be controlled by treating wastes before disposal . Recycling and recovery of materials from wastes is a viable method of reducing soil pollution .
2. The use of pesticides must be restricted as far as possible : biological control measures must be used instead . Fertilizers too , must be used moderately .
3. Industries must treat their wastes before disposal . Oil drilling sites should have proper waste and effluent pits.
4. Open cast mining should be discourage and effluent treatment plants should be used by the coal industry .

## Slide 35: Ecological Balance
In our earth , the living organism (ie biotic community) and non living (ie abiotic environment) are inter-related and interact upon each other . For example , plant do not live by themselves . Small and large animals belonging to different food habits are always associated with the plants . The plants and animal community interact with one another and together constitute a biotic community . There is interdendence between plants and animals of biotic community and interchange of materials place between them . Thus a tree provides food and oxygen to animals . The latter supply CO2 for the photosynthesis of green plants in presence of sunlight . Dead plants and dead animals and their excretions serve food for fungi and bacteria and as a consequence they are converted into organic humus component of soil

## Slide 36
As a result of further decomposition of organic matter, a number of elements such as Ca, K, Na and P are released and returned to the soil to serve as nutrients to the plants. The biological community thus interacts with the non-living environment and an exchange of materials take place between them . Thus there exist an ecological balance between living and non-living components on the earth . In the past the environment was pure, undisturbed, uncontaminated and basically most hospitable for living organisms . But the situation is just the reverse today , because progress in science and technology leads to pollution of environment, which has disturbed the delicate ecological balance . This ecological imbalance in the long run may prove disastrous for mankind .