## Slide 1: FUEL
Definition : Fuel may be defined as any substance which on being burnt in oxygen of air, produces a large amount of heat that can be utillised for domestic and industrial purposes. Eg coal,petrolium oil, coal gas etc are fuel
Classification of fuel : Fuels are classified into three general form .
Solid fuel 2.Liquid fuel 3. Gaseous fuel

## Slide 2
Solid Fuel
Natural : Wood , Coal
Prepared : Wood Charcoal , Coke
Liquid Fuel
Natural : Petrolium
Prepared : Various fractions of petrolium
Gaseous Fuel :
Natural : Natural gas
Prepared : Producer gas ,Water gas, Coal
gas etc.

## Slide 3: Properties
Ignition temperature : When a fuel is burnt , the evolution of heat takes place due to chemical reaction of it with oxygen of air and such process is called combustion. Thus heat energy is liberated from fuel by the process of combustion. In order to start active combustion, the fuel should be heated to a sufficient temperature. The minimum temperature at which active combustion of fuel takes place when the firring is once started is called as ignition temperature .
Flash point : Flash point in case of Liquid fuel is defined as the lowest temperature at which the fuel gives sufficient amount of vapour to form an explosive mixture with air. The higher the volatility ,the smaller the flash point.

## Slide 4
Fire point : The temperature at which the oil vapours will catch fire and continue to burn is called fire point.
Calorific value : The quantity of heat liberated is in proportion to the weight of the fuel. But the amount of heat produced by burning unit weight is the same for all kinds of fuels. The calorific value of any fuel is a measure of heat obtained by burning it and may be defined as the number of units of heat produced by the complete combustion of unit quantity of fuel.

## Slide 5
Caorific value may be expressed in different units.
eg, in case of solid and liquid fuels, it is expressed as calories per gm, Kilo calories per kilogram or British thermal unit per pound(BThU/lb)
For gaseous fuel it is expressed as calories/litre, calories/cubic meter or BThU/cu.ft.
1BThU = 252cal

## Slide 6
If we say that calorific value of a particular fuel is 2500 calories per gram, we mean that 1 gm of fuel on combustion gives 2500 calories of heat.
The calorific value of coal determined on as it is basis is called its gross cal value .
The calorific value of dry ash free coal is called net calorific value.

## Slide 7: Gross calorific value and net calorific value
All fuels contain hydrogen. In the determination of calorific value , this hydrogen is converted into steam and if the products of combustion are condensed to the room temperature , the latent heat of condensation of steam is also included in the heat measured,called gross calorific value. It may be defined as the total amount of heat produced when one unit of fuel has been burnt completely and the products of combustion have been cooled to 15oc or 60o F.

## Slide 8
When fuel is used ,vapour or moisture etc are not condenced and escape as such along with hot combustion gases. Thus a lesser amount of heat is available than expected. This is known as net calorific value and may be defined as the net heat produced when unit mass burnt and the products are allowed to escape.
Net Calorific Value = Gross Calorific Value –
latent heat of water formed
(Latent heat is10.56 Kcal mol- at ordinary temperature)
Thus Net Cal.Val. = Gross Cal.Val.- 10.56n
n= no of moles of H2 present in 1g of fuel.

## Slide 9: Solid fuel
Wood : It is an important domestic fuel throughout the world. It is composed of cellulose, some protein matter and resins. Freshly cut wood contains about 30-40% moisture, which can be reduced to 15-20% by burning in air. Wood burns with luminous and smoky flames. Calorific value of wood depend upon its variety but lies only between 4500 to 5000 kcal/kg.
Coal : Coal has been formed in nature as a result of the slow decomposition of vegetable and animal matter under the influence of heat, pressure and limited supply of air . Coal is found in various forms which represents the different stages of transformation of vegetable and animal matter.

## Slide 10
The 1st stage is peat, which contains a lot of organic matter and the carbon content being 60% its calorific value is about 5200 kcal/kg and approximate composition is C=60% ,H = 5.8%,
O = 33% and ash 1-2% . Peat is not important as a fuel.
The next stage is lignite . It is harder and contains about 67% carbon . Its calorific value is about 6500 kcal/kg and approximate composition is C=67% , H=5% , O=20% and ash= 8% .

## Slide 11
Another stage is Bituminous coal which contain about 83.5% carbon and high percentage of volatile matter. On distilation it gives large quantity of gases and Tar ,which are used in many industries. Its calorific value is about 8300Kcal/Kg and approximate composition is C=83.5%, H=5%, O=5% and ash =6.5% . The last stage of transformation is Anthracite coal which contain upto 90% carbon and least amount of volatile matter of all coals. It calorific value is about 8750 Kcal/Kg and composition is C=90% ,H=3% ,O=2%, Ash=5%.

## Slide 12: Pulverised Coal
Pulverised coal is obtained by grinding fossil coal . This is the principal kind of coal used in the cement industry. Combustion of fuel in the pulverised form offers the following advantages over the combustion of lumpy coal.
1. Pulverised coal burns quickly and completely owing to thorough mixing of pulverised coal with air necessary for combustion.
2. Easy maintenance of furnace due to simple control of combustion. The temperature of the furnace when pulverised coal is used can be easily increased or decreased by lowering or raising the rate of burning through a valve.

## Slide 13
3. There is a great possibility for more efficient utilization of low grades of fuel.
4. There is no formation of fuel bed as in the case of coal .Hence there is no clinker trouble as in the case of coal. Thus coal having high ash and clinker forming ash can be used fully burnt after pulverising it.
5. The pulverised coal can be handled easily like a liquid fuel and can be transferred through pipes.

## Slide 14
6. The atmosphere of the furnace when pulverised coal is used,can be maintained as oxidising or reducing. So this advantage is of great importance in metallurgucal furnace.
The fineness of pulverised coal depends upon concentration of combustible volatile and ash, densityof coal and the volume of combustion chamber available. Coal with a low concentration of volatiles should be ground more finely.

## Slide 15: The major disadvantages of pulverised coal
1.Considerable amount of ash carried over in the exhaust gases.
2. Deposit of molten ash on the boiler surface, creating hindrances to heat transfer.

## Slide 16: Destructive distillation of coal or Carbonization of coal
Thermal decomposition of coal is known as destructive distillation of coal.
When coarsely powdered coal is heated in a closed vessel or retort in absence of air, coal breaks down with the formation of ammonia, volatile matter and coke.
Carbonization of coal is carried out either at high temperature or at low temperature.
Low temperature carbonization (500-7500c)
High temperature carbonization (1100-14000c)

## Slide 17: By products of carbonization of coal
The by-products from either process are of the same type, but they differ in quality. The main by products are coal tar, coal gas , coke and ammonia.
Coal Tar : It is a black liquid. It is obtained in large amount from low temperature carbonization,which is an excellent source of phenol and nitrogen compounds. From high temperature carbonisation coal tar obtained in poor yield and it is the principal source of aromatic compounds such as benzene ,toluene ,naphthelene, anthracene etc .These are separated by fractional distillation of coal tar, which are starting material for different drugs ,perfumes ,explosives etc.Coal tar pitch is used for road making.

## Slide 18
Ammonia : High temperature carbonization yields more ammonia as then low temperature carbonization . It is converted into the fertiliser ammonium sulphate by reaction with H2SO4 .
Coke : Low temperature carbonization coke is soft and contain 8-20% volatile matter. It burns without smoke and therefore is used as domestic fuel . The coke produced by high temperature carbonization process is hard and largely used for metallurgical purpose . It burns with smoke .

## Slide 19
Coal gas : In low temperature carbonization much less coal gas is obtained, though it is of high calorific value .Coal gas is used for both heating and lighting purposes. Calorific value of coal gas is 4800 kcal /kg

## Slide 20: Liquid fuel
Petroleum : Crude petroleum is naturally occuring dark liquid found in the interior of the earth in widely separated regions of the world. It contains mixture of various hydrocarbons. The hydrocarbons are separated by distillation. The process of separation of various fractions is known as refining of petroleum.
Distillation of crude petroleum : Distillation of crude petroleum can be done in two methods-Gradual evaporation method and Flash evaporation method.The gradual evaporation method is obsolete now a days and flash evaporation method is widely implemented in modern plants. In flash evaporation method the crude oil is passed through heat exchanger (at 4000c)and then fed to pipe furnace.

## Slide 21
The volatile components from oil starts evaporating and they are made to pass through a fractionalizing column. The vapour rises through the distillation column and cooled in different collecting funnels. The vapours with higher boilling points condense first . The vapours having lower boilling points are collected at higher levels in the tower. The gases which can be liquefied under this conditions are collected at the top of the fractionating column. Bases on different temperature zones in the column, different products can be obtained. The various products with there boiling ranges and uses are listed in the table.

## Slide 22: products of fractional distillation of petroleum
Fraction Boiling range Uses
Petroleum 300 -900c As solvent and
ether dry cleaning
Gasoline 700 – 2000c As motor fuel,
or dry cleaning etc
Petrol
Kerosene 1750 – 2750c As fuel and
illumination

## Slide 23
Fuel or Above 2750c For diesel
Diesel oil engines and
furnaces
Lubricating Above 3000c As lubricants
oil
Residuel Above 3500c Source for
oil paraffin wax,
asphalt etc.
and used for
candles,
vaseline,
paints,road
surfacing etc.

## Slide 25: Classification of Petroleum oil
The crude petroleum may be devided into the following three classes.
1. Paraffin Base : If the residue obtained after removal of volatile compounds of crude oil is rich in paraffin wax, the petroleum is called paraffin base. These crudes consist primerily of open chain compounds and furnish low octane number gasoline.
2. Asphalt or Naphthene Base : If the residue obtained after removal of volatile compounds of crude oil is rich in naphthenes (cycloparaffins) it is classified as asphalt or napthene base. These crudes contain high percentage of cyclic compounds and furnish relatively high octane number gasoline.

## Slide 26
3. Intermediate Base : If the residue left after removing volatile compound of crude oil contains parafins and naphthenes both, the petroleum is called intermediate base. Hence these crudes contain large quantities of both paraffins and naphthenic compounds and furnish medium grade gasoline.
Crude oil from pensylvania,Iran,Iraq and Rumania has been found to be paraffinic and that obtained from Baku (Russia) and venezuela is asphaltic. Crude oil from Texas and Mexico has been found to be both paraffinic as well as asphaltic.

## Slide 27: Properties of liquid fuel
Properties that are taken into consideration are 1.Viscosity 2. Specific gravity 3. Flash point 4. Octane number.
Viscosity : It is the number of dynes required to move per sq.cm. of the liquid over a layer of 1sq.cm. area and one cm distance with a velocity 1 cm/sec.
Specific gravity : Specific gravity is the ratio of the weight of any volume of the substance to the weight of an equal volume of water at 40c .
Sp.gravity = ----------------------------------------
Wt. of same volume of water at 40c
Wt. of any volume of the substance

## Slide 28
Octane number : Octane number of a fuel is a measure of its tendency to knock . Knocking is sharp metallic sound produced in the internal combustion engine owing to immature ignition of the air –gasoline mixture. The hydrocarbon “isooctane” (2,2,4 trimethyl pentane)
CH3 CH3
CH3-C –CH2- CH-CH3
CH3
which was found to be free from knocks was arbitrarily given an octane number 100,whereas n-heptane
(CH3-CH2-CH2-CH2-CH2-CH2-CH3) which nock badly was rated at 0.

## Slide 29
Now if the two hydrocarbon viz iso-octane and n-heptane are mixed in all proportions , a series of fuels having octane number from 0 to 100 are obtained . Such mixtures of isooctane and n-heptane are taken as standared and the knocking property of other fuel is compared to them. The percentage of isooctane in the mixture is known as the octane number.
Thus octane number of fuel is defined as the percentage of isooctane present in a mixture of isooctane and n-heptane when the mixture has the same knocking performance in the experimental engine as the fuel under examination.

## Slide 30
A fuel is said to have octane number 70 if its tendency to knock in the test engine is same as that of a mixture of 70 percent isooctane and 30 percent n-heptane . Higher the octane number of a fuel less will be its knocking tendency. So high octane number is recommended for good fuel.
The straight chain alkanes are very poor fuels and cause the engine to knock. While the use of branched chain hydrocarbon and alkanes eliminates the knocking considerably. The addition of tetraethyl lead also improves the antiknocking character of fuel.Antinocking compounds are- TEL, MMT,Methyl cyclopentadienyl , Ferrocene, Iron carbonyl,Isooctane etc.

## Slide 31: Gaseous fuel
Name, Composition and uses of some commercial gaseous fuel
1. Natural gas
Composition : 85% Methane (CH4)
10% Ethane (C2H6)
5% other hydrocarbons
Calorific value : 1200 to 1400 kcal /m3
use : Used in industry as well as in domestic
purposes. Various by products from Natural gas
are of great industrial importance.These are methane,
ethane, propane, butane, natural gasoline and LPG etc.

## Slide 32
2.Producer gas
Composition : 30% CO
52% N2
13% H2
3% CH4
2% CO2
Calorific value: 1000 to 1300 kcal
Use : It is the cheapest fuel gas in terms of heat per unit. It is largely used in various furnaces and for running gas engines.

## Slide 33
3. Water gas :
Composition : 51 % H2
41% CO
4% N2
4% CO2
Calorific value : 2800 kcal/m3
Use : Water gas mixed with hydrocarbon gases is called carburatted or enriched gas, which is used as fuel and as an illuminant.

## Slide 34
4. Coal gas :
Composition : 45% H2
35% CH4
8 %CO
6% N2
2% CO2
4% other hydrcarbons
Calorific value : 4800 kcal/m3
Use : Used as fuel and as an illuminant .

## Slide 35: Manufacture of Producer gas
It is formed by blowing controlled amount of air through a deep bed of red hot coke or coal. Instead of passing only a blast of air a mixture of air and steam is generally preferred.
The apparatus in which the gas is made called producer. It consists of a large air tight cylindrical furnace made of sheet-iron lined with fire bricks. It is provided with an inlet at the bottom through which a mixture of air and steam can be blown and an outlet for the escape of producer gas at the top. From the top ,there is a device of adding fresh coke and at the bottom there is an arrangement of removing the ash. The producer is filled with coke and mixture of air and steam is passed from the bottom.

## Slide 37
O2 in air reacts with hot carbon and produces CO2.
C + O CO2 + 97 kcal
When CO2 moves up through the upper layers of hot coke , CO2 is reduced to CO , by red hot coke .
CO2 + C CO + 39kcal
Here steam also reacts with hot coke producing CO and H2 .
C + H2O CO + H2 - 29 kcal
The gas thus escaping out through the outlet, consist of mixture of CO, H2,CO2 and large amount of N2 (from air).

## Slide 38: Manufacture of water gas
This gas is prepared by passing a blast of steam through a deep bed of red hot coke in a chamber , called producer. Here steam react with coke to produce CO and H2.
C + H2O CO + H2 - 29 Kcal.
This reaction takes place at 10000c and it is endothermic . Thus heat is absorbed and therefpore after some time temperature of coke begins to fall below 10000c . At this lower temperature again steam react with coke to give CO2 and H2.
C + H2O CO2 + H2 - 19 Kcal.

## Slide 39
Then supply of steam is stopped and a blast air is blown to heat the coke to the required temperature. Carbon reacts with O2 to form CO and CO2 and the reactions are exothermic .
C + O2 CO + 59 Kcal.
C + O2 CO2+ 97 Kcal.
When the temperature of the coke is increased to the desired level , steam is again blown until the temperature falls sufficiently. The air is blown throw again to increase the temperature .The blowing of air is continued for about 2 minutes. Such period is called blow period .

## Slide 40
During this period the gas coming out is not water gas but a mixture of CO,CO2 and N2 This period is followed by steam blast which is called the run period and is continued for about 4 minutes .During this period water gas is produced which contain H2,CO,CO2 and N2.

## Slide 41: Bio gas
Bio gas is produced by decomposition organic matter in the absence of oxygen (anaerobic digestion).Oranic matter includes dead plants and animal material,animal excretaandkitchen waste etc.When cattle dung is used as primary material in the production of biogas then the generated gas is termed as gobar gas.
Cow dung when subjected to the action of a kind of microorganism in closed tank(called digester) undergoes a type of fermentation and converted into gobar gas which is a mixture of CH4 ,CO2 and minute quantities of other gases. In addition , a slurry rich in N2 is also obtained which is used as a manure for the fertility of agricultural lands.

## Slide 42
the biogas generator consists of steel diester, set under ground by a cement concrete work. The tank is closed one receiving the charge of bacteria and cow dung. The charge consists of cow dung and water in the form of a slurry. The slurry is kept in the tank for about 4 weeks, at temperature in between 350 – 500c. About 160 litres of gobar gas is produced per kg of cow dung. The average composition of bio gas is
CH4 = 55%
CO2 = 35%
H2 = 7.4%
N2 = 2.6%
H2O = traces

## Slide 44
Calorific value of this gas is 5300 Kcal/m3 .
Biogas is clean unpolluted and cheap source of energy in rural areas. Use of biogas in rural areas prevents cutting of trees and thus helps in ecological balance.
A limitation of biogas is however its dependence on cattle dung , from which it is prepared. Another limitation is to have the gas burner within 10 metres of the plant.

## Slide 45: Liquefied Petroleum gas(LPG)
LPG is odourless, colourless,non-toxic ,flammable mixture of combustible gases of hydrocarbons primarily butane and propane. It can be prepared either by petroleum distillation or cracking of hydrocarbons. Based on method of preparation ,the composition of LPG may vary to some extent. However ,the average composition of LPG is
n- Butane 27%
Isobutene 24%
But-1-ene and but-2-ene 2.4-2.8%

## Slide 46
For domestic purposes it is supplied in pressurised steel cylinder.The pressure of LPG within the cylinder is about 3kg/cm2 .The pressure decreases to 0.034kg/cm2 by the operation of the regulator of the cylinder during let off stage. LPG is heavier than air and thus will flow along the floor and tend to settle at basements. This may lead to explosion if the mixture of LPG and air is right and if there is an ignition source.
For risk management the LPG in supplied
cylinder is mixed with an odorant like
ethanethiol so that leaks can be detected more
easily.

## Slide 47
Calorific value of LPG is about 29780 kcal/m3 .
LPG is used as domestic fuel, direct motor fuel and as a source of petrochemicals.

## Slide 48: Advantages of solid fuel over liquid fuel
1. Solid fuel can be very conveniently stored due to their high ignition temperature.
2.They are comparatively cheap.
Disadvntages of solid fuel
Only a few percentage of calorific value is actually utilized for useful work ,a large portion of the heat is wasted.
A large amount of unburnt fuel is also wasted along with clinker.

## Slide 49: Advantages of liquid fuel over solid fuel
1. The liquid fuels burn freely with high efficiency when once ignited and at once the required temperature can be achieved.
2. They do not leave any ash or residue.
3.They are economical and convenient for transportation.
4. Combustion of the liquid fuel is uniform and therefore uniform heating power is attained.
5. The fire can be distinguised when desired. So
there is no wastage of fuel.

## Slide 50
Disadvantages of liquid fuel
A great precuation should be taken for storing liquid fuel because most of them are inflammable.

## Slide 51: Advantages of Gaseous fuel
1. The gas can be distributed over wide area by pipes from the source.
2. Have high calorific value.
3. They are smokeless easy to ignite and do not leave ash.
Disadvantages of gaseous fuel lie in the danger of explosion and large scale fire it may cause.
Disadvantages of gaseous fuel