## Slide 1: Water
Natural water may be devided into two classes- soft water and hard water
Water which gives good lather immediately when treated with soap is called soft water.
Water which does not give lather when treated with soap is called hard water.
Hardness of water caused by the presence of dissolved salts such as bicarbonates ,sulphates and chlorides of Ca and Mg.

## Slide 2
Types of hardness:
Temporary hardness
Permanent hardness
Temporary hardness : It is caused by the presence of bicarbonates of Ca and Mg. The hardness is called temporary because it can be removed by easy means like boiling.
Permanent hardness : It is caused by the presence of sulphates and chlorides of Ca and Mg . This harness can be removed by easy means like boiling ,so it is called permanent hardness.

## Slide 3
Disadvantages of using hard water in boiler
Water is used in boilers for generating steam. Impurities present in water has serious bad effects for such steam boilers.
Formation of Scale of or Sludge : When hard water is evaporated in the boilers the salts of Ca,Mg and others impurities like silica and alumina come out in the form of residue. The residue settles inside the boiler and in due course adhere to the metal surface . It is called sludges or scales.
Bad effects of Scales : The scales are hard and bad conductors of heat. So when scales are formed much heat is lost unnecessarily and the regular supply of steam is stopped.

## Slide 4
To maintain regular supply of steam extra heat should be given .As a result extra amount of fuel will be required . So there will be wastage of fuel .
Again if extra heat is supplied the boiler material which is separated from water by the scale will be over heated and may become softer and softer. When it will be red hot the outer surface of it will quickly combine with atmospheric oxygen and will be converted into iron oxide. The inner red hot surface may react with steam and be converted into Fe3O4 .
Fe + H2O Fe3O4 + H2

## Slide 5
These Iron oxide is non-adherent and comes down as slude. So the boiler material is ruined and the life of the boiler is shortened .
On over heating there will be un-necessary strain on plates and tubes, so they will be damaged soon.
On over heating the boiler material and scale will expand . But because of un-equal expansion, the scale would get cracked.

## Slide 6
Then boiler water will at once come in contact with red hot plates of the boiler where scale is cracked and will immediately be converted into steam with the result that there may sudden rise of pressure inside the boiler which may lead to a dangerous explosion.

## Slide 7
0 - 50 ppm Soft
50 – 100 ppm Moderately soft
100 - 150 ppm Neighther soft nor hard
150 - 200 ppm Moderate hard
200 – 300 ppm Hard

## Slide 8: Softening of water
The process of removing soluble calcium and Mg salts from hard water is called softening of water.
Softening of temporary hard water
By boiling : Temporary hardness of water can be removed by boiling . Temporary hard water contains Ca and Mg bicarbonates. These salts are decomposed on boiling the water forming insoluble CaCO3 and MgCO3 which can be removed by filtration and thus water become soft.
Ca(HCO3)2 CaCO3 + CO2 + H2O
Mg(HCO3)2 MgCO3 + CaCO3 + CO2 + H2O

## Slide 9
Clark’s method : In this method sufficient amount of lime is added to the water which convert all the soluble bicarbonates into insoluble carbonates as shown below.
Ca(HCO3) + Ca(OH)2 2CaCO3 + 2H2O
Mg(HCO3) + Ca(OH)2 CaCO3 + MgCO3
+ H2O
To much excess of lime should not be added , otherwise it would harden and not soften the water.

## Slide 10
Softening of Permanent hard water
By adding washing soda :
Permanent hardness of water can be removed by adding calculated quantity of Na2CO3
CaSO4 + Na2CO3 CaCO3 + Na2SO4
MgCl2 + Na2CO3 MgCO3 + 2NaCl
Temporary hardness can also be removed by this method.
Ca(HCO3)2 + Na2CO3 CaCO3 + 2NaHCO3

## Slide 11
Zeolite or Permutit process :
This is a modern process for removing both temporary and permanent hardness of water. Permutit is Sodium Alumino silicate Na2Al2Si2O8 The remarkable property of this sodium permutit is that when it comes in contact with hard it exchanges its sodium with the Ca and Mg to form insoluble Ca and Mg permutit.
Sodium permutit is placed in a suitable container and hard wateris allowed to pass throuh it . The Ca and Mg salts react with permutit forming Ca and Mg permutit. These are insoluble and therefore can not pass through the filterbed. The harmless soluble Na salts will go into the water.

## Slide 12
Na2Al2Si2O8 + CaSO4 Ca2Al2Si2O8 +
Na2SO4
Na2Al2Si2O8 + MgCl2 MgAl2Si2O8 +
NaCl
If this process is continued for about 12 hrs, all the sodium in the permutit are replaced by Ca and Mg and then this permutit can not remove the hardness of water. So to regenerate this permutit for further use a strong solution of NaCl is passed through Ca and Mg permutit, when Ca and Mg exchanges with Na forming Na permutit and Chlorides of Ca and Mg . Ihis chlorides of Ca and Mg is then washed out.
CaAl2S2O8 + NaCl Na2Al2S2O8 + CaCl2

## Slide 14
Treatment of water for town supply:
Treatment of water to make it suitable for drinking purpose is carried out in the number of steps.
1. Sedimentation : It is done to allow the insoluble impurities to settle down at the bottom of the tank of water.But this plain sedimentation can not remove the finely devided and colloidal impurities as their settling velocities are very low. It is therefore necessary that these smaller particles are converted into larger ones with higher settling velocities. This is done by coagulation . For this purpose certain chemical known as coagulants are added to water in the tank and thoroughly mixed.

## Slide 15
The coagulants react with alkaline salts present in water and form a thick gelatinous precipitate known as flock . This flock has a property of attracting fine particles and colloids to formbi flock and then settles rapidly. The most common coagulants used for this purpose are Alum(K2SO4 Al2(SO4)24H2O), Iron sulphate etc.
2. Filtration : Water from the sedimentation tank comes in at the top of the filter plant and seeps through the layers of fine sand, coarse sand and gravel . Thus rest of the suspended matter are taken out from the water.

## Slide 17
3. Sterilisation or disinfection :
After removal of suspended impurities by sedimentation and filtration, water is then disinfected to eliminate completely the injurious bacteria. The following treatments can be used for sterilisation of water.
Boiling : By boiling water all the germs and bacteria are killed. But this method can be used only for household purposes, this process is not applicable for town supply.
2. Chlorination : Chlorine in its various forms is
often used in sterilising water for town supply.
Generally for chlorination of water in town supply
Bleaching powder is added. It eliminate bacteria,
also helps in prevention and destruction of odour
and colour.

## Slide 18
3. Ozonisation : Another effective method of sterilizing water is by the use of ozone. Ozone easily splits up into nascent oxygen which oxidises harmful matter and kills bacteria.
This method is little expensive and hence is not used to sterilize water on large scale.
4. Aeration : In this process the water is purified by exposing it to air .Water can be aerated by spraying it into the air through the spray nozzles. By the exposure of water to air the bacteria is killed and organic matters are oxidised.
In this case a large surface area is reqired and another disadvantage is that the exposure time is about 2 seconds which is very less.

## Slide 19
5. Ultraviolet rays: The invisible ultra violet rays are also very effective in killing all type of bacteria . These rays are generated by passing electric current through mercury vapour bulb. By this rays various kinds of germs are killed in short time.
Water after purification is supplied for drinking and other domestic purposes.