## Slide 1: FABRIC MANUFACTURE-lll
Weft insertion by Projectile
Weft insertion by Rapier
Weft insertion by Air jet
Weft insertion by other methods
Weaving certain commercial Fabrics
Non-woven Fabrics

## Slide 2: Weft insertion by Air jet
Weft insertion by Air jet has made a major entry in early 70s
Its importance is increasing because its ability to weave a wide range of fabrics at a very high insertion rate of about 2000 mpm.
Fabric width is restricted to about 150 cm.
Low noise level produced than other conventional method of picking.
The first commercial airjet weaving m/c was the “Maxbo” designed by Maxbo Paaeboe.
Later Maxbo Murata started to produce the m/c commercially.

## Slide 3: Working principle of Maxbo Murata
Weft yarn is measured by a drum equivalent to the cloth width
Tensioner loosens the weft yarn prior to weft insertion
After picking , the slack yarn is drawn back and nozzle spouts the weft yarn by compressed air
Suction tube is placed on the offside of the loom guides the inserted weft and inhales the weft end which is cut by the cutter

## Slide 4: Passage of warp on Maxbo Murata Loom
Weave plane of original Maxbo Murata Loom was 360 , later modified to 450 to vertical with healds displaced from horizontal.
This system has difficulty in drawing in ends through healds and reed.

## Slide 5: Disadvantages of Maxbo Murata Loom
Since the air stream emerges through the main nozzle and it is controlled by two cover plates ,the weft thread can be propelled through warp shed upto a certain distance and loom width is limited to 110 cm only.
Only tappet shedding upto 8 heald shafts can be used
Not suitable for heavy fabrics
Count range is from 20-100 dtex.

## Slide 6: Contd.
The projected weft ends on both sides are tucked into the next shed by special tucking-in device and woven in next pick.
The projected weft ends on both sides are tucked into the next shed by special tucking-in device and woven in next pick.
The reed is not reciprocated as in shuttle loom. It rocks about its axis by a pair of cams.
The reed and projectile guides are stationary during picking.
A sley dwell of 255 degree at back centre enables the safe journey of the projectile.

## Slide 7: Contd.
Smaller depth of shed for smaller size projectile than shuttle as in shuttle loom.
Weft insertion rate upto 900 to 1500m/min. is possible depending on type of loom and reed width.
The colour changing mechanism is less complicated
Facility to insert two picks in the same shed without the use of a dobby.
In case of weft breakage the take-up beam and heald frames can be driven in reverse direction by a pick finding mechanism.

## Slide 8: Advantages of projectile weaving m/c
Two or three clothes can be woven simultaneously
Breakage rate is almost 50% compared to shuttle loom. It may be due to smaller shed, reed with higher air to wire ratio and/or beat up line nearer to centre of the reed.
Since the projectile passes through the shed there is no reed to projectile or projectile to yarn contact.
With the four/six colour weaving machine the mechanical problems of conventional looms are eliminated.

## Slide 9: Projectile Picking Mechanism features
Different from conventional picking system
Heavy wooden shuttle (approx.400g) is replaced by a 40g fine steel gripper(90mmx14mmx6mm)
Weft is drawn directly from a large weft package (approx. 2 kg.).No weft winding required.
Picking takes place from one side only.
Picking energy is derived from the energy stored in a metal torsion bar, which is twisted at a predetermined amount and released to give a high rate of acceleration.
Due to small mass of projectile compared to wooden shuttle, very high velocity is achieved ie twice as those in conventional shuttle.

## Slide 10: Projectile Picking Mechanism

## Slide 11: Projectile Beat-up Mechanism
Different from conventional beat-up using crankshaft, crank and crank arm
Sley is positively rocked about its centre by means of matched cams
A saddle carrying two antifriction rollers is attached to the sley and these rollers bear against the surface of the cams.
There are several pairs of cams across the width of the sley
The sley carries the reed and a no. of projectile guides
Mass of the sley is about 16 kg (220 cm loom),small compared to that of shuttle looms

## Slide 12: Contd.
Projectile guides are used for the smooth movement of the projectile through the shed
During beat up projectile guides move down the shed and lie below the cloth near the fell.
Because of the cam operated sley it is possible to have a dwell period of 2550 at its back centre.