## Slide 1: Assam Textile Institute
Subject- Garment Construction-II
Semester- IV

## Slide 2: Unit-I Clothing Construction
1.1.1- Seaming special fabric
The most important properties of a seam are strength and flexibility and these are determined by a number of technical factor plus the characteristic of the fabric and the width of the seam.
The width of the seam is primarily decided by the characteristic of the fabric to be sewn and the type of seam being sewn.
1.1.2- Fullness Techniques
  Darts-
  Darts are meant to dispose of surplus material in clothes and to give a good fit according to the curvature of a figure. The dart should be very carefully placed, so that they reduce that the material at the exact position in garment.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 3: Unit-I Clothing Construction
Types of Darts in Clothing: The different types of darts are discussed below:
  Straight dart: Straight darts have only one point with dart legs along the edge of the pattern.
  It is a straight line of stitching
  from the point to the seam line
Bust darts: Bust darts usually start the side seam of a garment and end near the
apex of the bust in order
to make the bodice of a
garment more form fitting.
.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 4: Unit-I Clothing Construction
French darts: French darts are a type of elongated bust dart that start at the side seam, down near the waistline, and end up near the bust point.
Double pointed dart: This dart is unique as it tapers in a straight line from the middle to both the ends
.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 5: Unit-I Clothing Construction
Tucks-
In sewing a tuck in fabric that is sewn in place. Tucks are stitched folds of fabric mainly used to decorate garments. Sometimes, released tucks may be used for shaping the fabric to the body.
• Pin tucks:
These are minor ones.
.• Spaced tucks:
These tucks have gaps or spaces
between the stitching.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 6: Unit-I Clothing Construction
Knife pleat:
Knife pleats can be used as an alternative for gathers. These pleats
generally have a width of
about 1/2–2″ and are turned
towards the same direction.
Box pleats: A box pleat is formed when two consecutive knife pleats are folded in
opposite directions – one to
the left and one to the right.
This is used in frocks and skirt
waistline.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 7: Unit-I Clothing Construction
Inverted pleat: Inverted pleats can be obtained by reversing the box pleat. An inverted pleat
is made while two knife pleats
are twisted nearer to each other
in a manner that the folds meet
in the centre on the face side of
the garment. These kinds of pleats
are utilized commonly in uniforms and skirts.
Kick pleat: Any of the above discussed pleats like knife
pleat, box pleat or inverted box pleat
could be used to construct
kick pleats in skirts.
After pleating, a top stitch
is made near the fold and
extended to the desired length
and the decorate as required.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 8: Unit-I Clothing Construction
Gathers Gathering is a basic sewing technique that shortens the length of a piece of fabric. Generally it is used to manage fullness in a stitched project. It is done so that the longer piece can be attached to a shorter piece. A few places where gathering is used are when making ruffles, setting in puffed sleeves, or attaching a skirt to a bodice. Gathering technique is easier to create on lighter fabrics. Gather enhances the garment appearance but it also used for functions. Generally it can be noticed at the waistline, neckline, yoke line and upper and lower edge of the sleeve in the case of children’s and ladies garment. In general, gathering requires twice the amount of fabric as that of the waist circumference measurement.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 9: Unit-I Clothing Construction
Gathering by hand: Gathering is achieved by fastening a thread followed by securing with two rows of tack stitches. The ends of the thread are drawn until the section measures the desired length and the thread is wound around over a bell pin. Fabrics of any weight can be gathered using the hand and the size of the folds can be easily changed by varying the width of the stitches, which cannot be performed in a machine
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 10: Unit-I Clothing Construction
Gathering by machine:
The machine is adjusted to produce long stitches and the upper tension is reduced slightly. With such a configuration, two rows of machine stitches, each 1/4″ apart, are made. Both the bobbin threads are pulled together and stitched to evenly distribute the fullness. For gathering large sections of fabric, the specialized attachments in sewing machine such as gathering foot or gathering ruffles could be used. Gathering by machine is much faster for lightweight fabrics like voile, organza, netting, cotton lawn, etc. Usually, two rows of machine stitching are done down the length to gather 1/4″ from the edge and 1/4″ apart.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 11: Unit-I Clothing Construction
Shirring-
In sewing, shirring is two or more rows of gathers used to decorate parts of garments, usually the sleeves, bodice or yoke. The term is also sometimes used to refer to the pleats seen in stage curtains. Shirring is a method of shaping a garment and is done so by controlling fullness. Its technique is similar to gathering. Shirring consists of two or more rows of gathered fabric. Shirring can be a pretty and feminine alternative to darts in small areas of a garment. Shirring can also be done on large areas of a garment like all around the top of a full skirt. Shirring works best on soft fabrics but can also done on stronger fabrics.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 12: Unit-I Clothing Construction
Smoking-
A full work shirt was gathered at the bodice and the sleeves. This gathered effect in the garment was then called a “smock”. Smocking was introduced to work man garment mainly to give fullness or free movement of their body and arms. Smocked garments were worn by agricultural laborers, trades men and shepherds in earlier times.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 13: Unit-I Clothing Construction
Ruffles-
In sewing and dressmaking, a ruffle, frill, or furbelow is a strip of fabric, lace or ribbon tightly gathered or pleated on one edge and applied to a garment, bedding, or other textile as a form of trimming.
Single edge Ruffles
This is a single strip of fabric gathered along one edge and stitched to the edge of a garment. The raw edge of this strip is usually finishes with any of the fabric edge finishes.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 14: Unit-I Clothing Construction
Double edge ruffles
This is a single strip of fabric gathered in the middle. The result is two edges of ruffles along the middle stitching line.
Topic-
1.1 Definition
1.1.1. Seaming special fabrics
1.1.2. Fullness Techniques
    Darts
    Tucks
    Pleats
    Gathering
    Shirring
    Smoking
    Ruffles

## Slide 15: Unit-II Finishing Techniques
2.1.1-Neckline
The neckline is the top edge of a garment that surrounds the neck, especially from the front view. Neckline also refers to the overall line between all the layers of clothing and the neck and shoulders of a person
U-shape neckline-
A U-neck opening on a shirt is basically what you would expect
from the name. The neck
opening of the shirt is formed in
the shape of the letter “U”
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 16: Unit-II Finishing Techniques
Round neckline-
It is a round neckline which
sits close to the neck, typically
seen in t-shirts. It usually
ends above the collarbone
and usually has a band around it.
V- shape necline-
These are formed by two diagonal lines from the
shoulders that meet on the
chest creating a V shape.
The depth of the V
can vary, ranging from
demure styles to plunging.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 17: Unit-II Finishing Techniques
2.1.2- Plackets
Plackets are openings in woman’s garment such as a skirt or blouse, either where it fastens or in a pocket. Plackets are particularly seen in women’s garments which have a good fit. They can also be found at the cuff of a sleeve in a garment. Plackets facilitate easy usage of clothing and are sometimes used as a component for enhancing the design. In modern usage, the term placket often refers to the double layers of fabric that hold the buttons and buttonholes in a shirt. Facings or bands are attached in a modern placket to incorporate buttons, snaps or zippers. In designer garments, a placket is a double layer of fabric that contains buttons and buttonholes in a skirt. Plackets are made by interfacing more layers (generally more than one) of a fabric to impart strength and support to the garment as it is subjected to stress when worn . To protect the wearer from fasteners coming in contact with their skin and to hide underlying clothing, the two sides of the plackets are overlapped.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 18: Unit-II Finishing Techniques
Different Types of Plackets in Garments: 1. Continuous lap sleeve placket: A continuous lap sleeve or
bound placket is a common
finish that facilitates dressing
ease in blouses and shirts
2. Two-piece placket: This kind of placket is mostly used as an opening in the left side of skirts or
in petticoats and sometimes
in the back side of dresses.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 19: Unit-II Finishing Techniques
2.1.3- Pockets-
Pocket is a bag or envelope which an opening or slot with a closed end that is usually sewn in or over the garment. In older usage, a pocket was a separate small bag or pouch. Pockets may have a decorative or functional purpose. Sometimes pockets can be used for both purposes
Different types of pockets in garment
Patch pocket-This pocket is as named added as a patch on the garment. It is
also the most common type
of pocket. You must have seen
patch pockets on shirt fronts.
It can be of different shapes
like square, rectangular, round
and even triangular.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 20: Unit-II Finishing Techniques
Slash pocket- It starts from the waist and goes diagonally down to the sides.
This pocket is a kind of back
facing to the front of the
garment. Sometimes it is
shaped as a curve or as straight
but slanted. They are also called
cutaway pockets.
Welt pocket- This is a slit pocket where the slit is finished with a band of a
separate piece of fabric o
r a welt. Besom Pockets are
inset pockets seen on a man’s
suit jacket made with a narrow
welted edge above the pocket
opening.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )

## Slide 21: Unit-II Finishing Techniques
Flap Pocket-This pocket has a flap covering the slit of the pocket. This type of
pocket is usually seen in
formal clothes like jackets.
The pocket is usually a patch
pocket.
Inseam pocket- In seam pockets are sewen along the side seams of the garment.
These pockets are made on
the left side of the garment.
These pockets are generally
stitched in boy’s shorts,
girl’s pant, pajama and kurtas.
Topic-
2.1-
Perform the given finishing work on the stitched garment.
2.1.1- Definition of necklines, Finishing of U , round, V and fancy necklines.
2.1.2- Finishing of placket opening of upper and lower garment.
2.1.3- Pockets ( Definition of pockets, finishing of patch pockets, Slash pocket, double welt pocket, in seam pocket, front hip pocket )